## Slide 1
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
SMART IOT WEATHER STATION
Real-Time Microclimate Monitoring with ESP32, DHT22, SSD1306 & Cloud Analytics
MENTOR:
[Faculty Mentor Name]
Department of ECE, GCET
PRESENTED BY:
1. Prasoon (Roll No: ________________)
2. Team Member 2 (Roll No: ________________)
3. Team Member 3 (Roll No: ________________)

## Slide 2
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CONTENTS
❖ 01. Introduction
❖ 02. Motivation
❖ 03. Objectives
❖ 04. System Architecture & Hardware Description
❖ 05. Software & Cloud Integration (ThingSpeak & Vercel)
❖ 06. Results & Real-Time Performance
❖ 07. Conclusion & Future Scope
❖ 08. References

## Slide 3
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
INTRODUCTION
• Rapid Urbanization & Microclimate Shifts: Localized meteorological variations significantly impact human health, agricultural yields, industrial workspaces, and smart city infrastructure.
• Limitations of Conventional Weather Stations: Traditional weather monitoring systems are bulky, expensive, lack cloud accessibility, and provide low temporal resolution with delays.
• The Role of IoT & Embedded Systems: Internet of Things (IoT) enables distributed, low-power, and compact sensing nodes that capture environmental parameters autonomously in real time.
• Core Implementation Technology: Utilizing the dual-core ESP32 microcontroller with integrated 2.4 GHz Wi-Fi to acquire high-precision temperature and humidity readings from a DHT22 sensor.
• Edge & Cloud Synergy: Sensor telemetry is simultaneously rendered locally on an I2C SSD1306 OLED display for immediate observation and pushed to ThingSpeak IoT Cloud for remote web analytics.

## Slide 4
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
MOTIVATION
✔ Hyper-Local Environmental Tracking
Regional forecast stations are located tens of kilometers away, failing to reflect microclimates in indoor labs, greenhouses, or localized urban zones.
✔ Occupant Thermal Comfort & Safety
Heat stress and humidity levels dictate thermal safety. Computing Heat Index and Dew Point on the edge aids occupational health and HVAC control.
✔ Affordable & Scalable Architecture
Off-the-shelf industrial weather loggers cost thousands of dollars. An ESP32 + DHT22 platform provides comparable fidelity under $15.
✔ Everywhere Access & Historical Trends
Eliminates physical data retrieval by pairing cloud streaming (ThingSpeak) with a zero-install, responsive web dashboard on Vercel.

## Slide 5
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
OBJECTIVE:-
• To design and fabricate an autonomous, low-power IoT Weather Monitoring Station using the ESP32 microcontroller.
• To interface a high-precision DHT22 (AM2302) sensor to acquire real-time temperature (accuracy ±0.5°C) and relative humidity (accuracy ±2%).
• To establish I2C communication with an SSD1306 0.96" OLED display for immediate local readout at the edge node.
• To compute thermal metrics (Heat Index and Dew Point) on-board to determine human comfort conditions.
• To stream sensor telemetry every 20 seconds to MathWorks ThingSpeak IoT Cloud using secure RESTful HTTP POST requests.
• To architect and deploy a modern, reactive web dashboard on Vercel with zero runtime dependencies and 24-hour canvas-based trend plotting.

## Slide 6
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
Description: Hardware Architecture & Interfacing
Component | Specification | Pin Interface | Role in System
ESP32 Dev Module | Xtensa Dual-Core 32-bit, 240MHz, 2.4GHz Wi-Fi 802.11 b/g/n | Micro-USB / 3.3V Power | Master controller, Wi-Fi telemetry & HTTP client
DHT22 (AM2302) | -40 to 80°C (±0.5°C), 0 to 100% RH (±2%), 0.5Hz rate | GPIO 4 (Single-wire digital) | Atmospheric temperature & relative humidity sensor
SSD1306 OLED | 0.96" Monochrome 128x64 display, I2C protocol | SDA: GPIO 21 SCL: GPIO 22 | Real-time edge telemetry display and connection indicator
Power Supply | 5V DC via USB / Mobile Hotspot Tethering | VIN / 3.3V LDO | Powers microcontroller, sensor, and display module
HARDWARE PIN INTERCONNECTION SCHEME:
• DHT22 VCC ➜ 3.3V | DHT22 DATA ➜ GPIO 4 (with 10kΩ pull-up) | DHT22 GND ➜ GND • OLED VCC ➜ 3.3V | OLED GND ➜ GND | OLED SDA ➜ GPIO 21 | OLED SCL ➜ GPIO 22 • Data Transmission Pipeline: DHT22 → ESP32 (Internal Math) → SSD1306 (Local) + Wi-Fi HTTP Post (ThingSpeak)

## Slide 7
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
Description: Software, IoT Cloud & Web Stack
ESP32 Firmware (C++ / PlatformIO)
• Reads DHT22 sensor via Adafruit Unified Sensor drivers.
• Calculates Heat Index (Steadman formula) & Dew Point (Magnus formula).
• Updates SSD1306 via Adafruit_SSD1306 wire library.
• Connects to Wi-Fi Access Point / Mobile Hotspot.
• Sends HTTP GET/POST to ThingSpeak API every 20 seconds.
ThingSpeak Cloud (MathWorks IoT)
• Channel ID: 3531601 (Public Open Data Access).
• Field 1: Ambient Temperature (°C)
• Field 2: Relative Humidity (%)
• Field 3: Heat Index (°C) | Field 4: Dew Point (°C)
• Timestamped cloud storage with REST API endpoint.
Frontend Dashboard (Vercel Deployed)
• Built with vanilla HTML5, CSS3, and ES6 JavaScript (Zero dependencies).
• Continuous live polling every 2s via fetch() with no-store caching.
• Dynamic HTML5 Canvas charting showing last 48 readings (~24 hours).
• Extremes detection (Min/Max temp & humidity) + Thermal comfort rating.
• Live production link: smart-weather-station.vercel.app

## Slide 8
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
Results & Telemetry Verification
LIVE SENSOR TELEMETRY READINGS
• Temperature (DHT22): 26.8 °C (Normal Room Condition)
• Relative Humidity: 69.8 % (Moderate-High Humidity)
• Heat Index (Computed): 28.5 °C (Perceived Temperature)
• Dew Point (Computed): 20.8 °C (Condensation Threshold)
• Upload Interval: Every 20 sec (ThingSpeak Cloud Rate)
• Web Refresh Rate: Every 2 sec (Real-Time Client Polling)
• Total Recorded Feeds: 58+ Feeds (Continuous Operation)
CLOUD DEPLOYMENT & METRICS VERIFICATION
✔ Zero-Latency Web Display: Real-time dynamic updates using fetch() API with auto-updating clock and status pulse indicator.
✔ HTML5 Canvas 24-Hour Graph: Dual-trace smoothed spline plots rendering temperature (°C) in coral and humidity (%) in teal simultaneously.
✔ Automatic Extremes Calculation: Computes session-wide Low and High markers on the fly from incoming feeds.
✔ Graceful Fallback Mode: Automatic visual alert ('ESP32 offline - connect to Wi-Fi') upon packet drop or network disconnection.
✔ Live Production Deployment: Hosted and globally accessible on Vercel CDN: https://smart-weather-station.vercel.app/ GitHub: github.com/prasoon9999/smart-weather-station

## Slide 9
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CONCLUSION & FUTURE SCOPE
CONCLUSION:
• A highly efficient, low-cost Smart Weather Station was successfully implemented combining embedded edge sensing with cloud computing.
• The DHT22 sensor and ESP32 demonstrated stable, accurate data acquisition with local OLED visualization and cloud transmission.
• The serverless web dashboard deployed on Vercel delivers seamless, responsive real-time graphical monitoring accessible globally from any web browser.
FUTURE SCOPE:
• Multi-Sensor Integration: Expanding hardware to include BMP280/BME280 for barometric pressure, rain gauge, and UV intensity sensors.
• Energy Harvesting & Autonomy: Integrating solar panels with TP4056 Li-ion battery charging and deep-sleep modes for off-grid deployment.
• Intelligent Alert System: Implementing Telegram / SMS / Email Webhook triggers for severe weather warnings and heat stress alarms.
• Predictive Machine Learning: Utilizing historical cloud feeds to forecast microclimate trends and rainfall probabilities.

## Slide 10
Galgotias College of Engineering & Technology, Greater Noida
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
REFERENCES:-
S. No. | Research Paper / Technical Standard / Datasheet
1. | Espressif Systems, "ESP32 Series Datasheet - 2.4 GHz Wi-Fi and Bluetooth combo chip," Espressif Inc., Version 3.9, 2023.
2. | Aosong Electronics Co., Ltd., "Digital-output relative humidity & temperature sensor/module DHT22 (AM2302) Datasheet," Guangzhou, China.
3. | K. S. Rao, V. S. Murthy, and T. P. Rao, "IoT Based Real-Time Environmental and Weather Monitoring System using ESP32," IEEE International Conference on Smart Technologies, 2021.
4. | MathWorks, "ThingSpeak Documentation: IoT Analytics with MATLAB Support and RESTful Web Services API," MathWorks Inc., 2024.
5. | N. H. Motlagh, M. Mohammadrezaei, J. Hunt, and B. Zakeri, "Internet of Things (IoT) for Climate Change and Weather Monitoring: Recent Advances and Applications," IEEE Access, vol. 8, pp. 62890-62908, 2020.
6. | Solomon Systech, "SSD1306 128 x 64 Dot Matrix OLED/PLED Segment/Common Driver with Controller Datasheet," Rev 1.1, 2018.

## Slide 11
THANK YOU
Questions & Answers
🌐 Live Dashboard: smart-weather-station.vercel.app 📦 GitHub Repository: github.com/prasoon9999/smart-weather-station